M5 SYSTEM—AN INTERPRETER FOR THE NASCOM ONE by Raymond Anderson
Nascom Implementation
The M5 interpreter was designed for implementation on small 8 bit microcomputers and the Nascom one standard system was an ideal choice because of its popularity and use of a fairly powerful processor (the Z80).
With only about 940 bytes available to the user, the language had to be compact enough to write decent programs in a small space, and also have a small interpreter to leave the maximum amount of spare memory. A simple editor was almost essential if programs of over about 50 bytes were to be written and debugged easily, and this required about 100 bytes.
The editor, interpreter and command mode are closely linked—for example, program variables are maintained over edits, and resets, and the editor will set up its cursor to inform the user where an error occurred.
A compact M5 program can be difficult to follow initially, so error routines which give the exact location and type of a run-time error are included, despite the penalty in RAM usage. (Execution speed is unaffected by error checking).
M5 is a very fast interpreter, although loops are not as fast as in machine code because each loop involves a small search. A well written M5 program will carry out general calculations at about 1/3-1/5 of the speed of machine code. (M5 programs are usually much faster to write and debug of course!)
The user may write programs of about 230 bytes in length—quite large in M5. Overlarge programs may cause trouble when entered, but the most likely indication of an overflow is a lot of garbage appearing on the end of the program when it is listed.
Introduction
The M5 system is entered by typing EC60 when M5 has been entered into user RAM. The prompt “M5:” should then appear at the bottom of the screen, indicating that the system is in the command mode. Commands which may be entered now are:

I	Input a new program and destroy the previous one. System responds with a newline and	waits for the user to enter a program. Input is terminated by a semi-colon, which returns	the user to the command made.
L	List the program currently in store and return to command mode.
R	Run the current program starting at the first symbol, after printing a newline.
E	Edit the current program, inserting the character pointer at the place the last instruction	was executed-or where an error was found. (See section on editor.)
RS	RESET the Nascom. This will cause a return to Nasbug. However, the current program	and value of X will be maintained ready for typing EC60 to resume programming.	RESET must also be used to stop a looping program.
Initialisation
When entering M5 for the first lime after loading it, it is best to initialise the user work area by entering and running a null program. This is done as follows: (Underlined characters are typed by the system.)

M5:Input	(i.e. type I)
;	(i.e. terminate input after entering nothing!!!)
M5:R	(Null program simply results in a carriage return.)
M5:	(System is now initialised.)
Other commands
M5 will respond with a new prompt to any unknown command letter.
Errors on input
A backspace will delete the last character only when in input mode. It may seem misleading if used to backspace up a line. (Try it and see!)
Backspaces can be inserted into a string in the program by using the INSERT command in EDIT mode. Semicolons are illegal characters inside an M5 program.
Shift-Backspace is a legal character in strings.
BASIC M5 LANGUAGE PRINCIPLES
M5 Arithmetic
The basic elements handled in standard M5 are 16 bit unsigned integers, which are adequate for most games and simple simulation or number manipulation. Numbers are in the range 0 - 65535 (decimal) and are modulo 65536 so 65536 seems the same as zero to the language.
Operators permitted in M5 are:
* (multiply) / (divide) + (add) - (subtract) £ (-1) &(+1)
the last two are included for faster execution if required, and for compact programming of loop control. (See later).
The Stack
An important aspect of M5 which is quite powerful once it is understood, is its stack based (Reverse polish) expression analysis. This system requires no parentheses and it can be used to evaluate arbitrary expressions quickly. The M5 algebraic system is similar to that found on some calculators and the analogy with a calculator is used in these notes.
The Current Value
On a pocket calculator, the Idea of a current value is easy to understand as it appears on the display and is often called "x". In M5 there Is also a current value (called "x”) and it is altered only in the following circumstances:
1. If a number appears in the program (not in a string) x takes its value.
2. On encountering an identifier A-Z x takes the value stored there.
3. On encountering a ? (not after = ) x takes its value from the keyboard.
4. After a diadic operator (/ - + *) x becomes the result.
5. If x is incremented or decremented (using & or £).
Variables
As in most other languages, M5 has variables A-Z and a special one @. One of these variables becomes current by simply quoting it in the program. (point 2 above).
x may be stored in a variable by simply using =k where k is a variable name.
If =? is used, the current value (x) is displayed as a decimal number on the screen. (This is how numbers are output in M5).
EXAMPLES (These are all legal M5 programs- Try if unsure!)
(i) A	What is in location A is now also in x (the current value).
(ii) ABC	x takes on the values in A then B then C and keeps the value C.
(iii) 23	x becomes 23.
(iv) 23A	x becomes 23, then x becomes A (i.e., the number in A).
(v) 23 456	x becomes 23 and then x becomes 456.
(vi) A=B	x becomes A, then this value is stored in B.
(vii) A=B=C=D x becomes A . then this value is put into B, C and D.
(viii) A=?D=?	x becomes A and this is displayed, then x becomes B and is displayed.
(ix) =?=A	what is in x (left from last program) is displayed and put in A.
N.B. If you want to check what is going on, put the characters: =? in your program and x at these points will be printed.
For neatness and readability use: =? “ " which separates No’s by a space. E.G. 23=?” “ 11111 =? will produce: 00023 11111 as output if run.
Calculating
When a comma is encountered in an M5 program, the value of x is put on the top of the stack - pushing down all other members. We can represent the stack diagramatically to show what happens.
Imagine the M5 program: A,33,,BA Where initially A=l and B=2
        step: abcdefgh (could have run l=A2=3 before)
and follow it step by step:
STEP	SYMBOL	MEANS	x	top--STACK--bottom->	y (top element of stack)
a	A	Load A	1	- - - -	unknown
b	,	Push x	1	1 - - -	1
c-d	33	Load 33	33	1 - - -	1
e	,	Push x	33	33 1 - -	33
f	,	Push x	33	33 33 1 -	33
g	B	Load B	2	33 33 1 -	33
h	A	Load A	1	33 33 1 -	33

Note that the top member of the stack is called y.
So far, we have no means of removing items from the top of the slack. We do this by using operators such as + / * -
The operators work on x and y and put the result in x, removing y from the stack. Operators therefore do the following:
Operator	Function	Remarks
£	x := x - 1	This is the pound sign on the Nascom
%	x := x + 1	Much faster than ,1+ which is equivalent
+	x := x + y	y is lost. Overflow not detected (M5 2.1)
-	x := x - y	y is lost. Underflow not detected
*	x := x * y	y is lost. Overflowing bits put in @
/	x := x / y	y is lost. Remainder is put in @

EXAMPLES
Program: A,B+=?	Initially A=1 B=2
  step: abedef

STEP	SYMBOL	MEANS	x	y Rest of stack
a	A	Load A	1	? - - -
b	,	Push x	1	1 - - -
c	B	Load B	2	1 - - -
d	+	x:=x+y	3	- - - -
e-f	=?	Display	3	- - - -

The program displays the result of A+B. When run, 00003 is displayed.
Program to evaluate (2*3) + (7-2) and display it.
Program: 2,3*,7,2-+=?	Add result of 2,3* to 7,2-
  step: abcdefghijkl	and display the result
STEP	SYMBOL	MEANS	x	y Rest of stack
a	2	Load 2	2	? - - -
b	,	Push x	2	2 - - -
c	3	Load 3	3	2 - - -
d	*	x:=x*y	6	- - - -
e	,	Push x	6	6 - - -
f	7	Load 7	7	6 - - -
g	,	Push x	7	7 6 - -
h	2	Load 2	2	7 6 - -
i	-	x:=y-x	5	6 - - -
j	+	x:=x+y	11	- - - -
kl	=?	Display	11	- - - -

NOTE The operators # and & only affect x and are equivalent to ,1- and ,1+ (although faster and shorter).
Imagine we want to store the result of multiplying N by M in A. In Basic this Is A=M*N But in M5 this is M,N*=A
Here are some further examples of expressions:
BASIC	M5
Z = M*N*A	N,M*,A*=Z	or	N,M,A,**=Z
Z = (N+M)*A	N,M+,A*=Z
Z = (N+M)*(A-M)	N,M+,A,M-*=Z
Z = N*N	N,*=Z
Z = N*N*N*N	N,*,*=Z	or N,,,***=Z	(M5 only needs to get
N once)
Getting Data In
Data in M5 is Input from the keyboard. The program requests a number from the keyboard when it encounters a LOAD ? i.e., a ? in the program, not following =.
A number is terminated by any non numeric character. Usually the user will type a space after the number and the program will continue on the same line, otherwise he will use a newline after typing the number.
EXAMPLE ?,?*=? will prompt for a number, then another and print the product.
String print
Any string of characters surrounded by quotes “" is printed to the display exactly as written- including newlines etc.
e.g. “Input the number"
or “NEW
       LINE”
N.B. A jump will find labels in a string so beware of using ( in a string.
A nicer version of the program above Is:
“NUMBER" ?, "TIMES BY” ? *" IS “ =?
A newline is produced by a newline between quotes.
Loops and jumps
A way of repeating operations is almost essential in a programming language. In M5 this is done by using using jumps and labels.
A label is represented in M5 by (n where n is any symbol which an be entered at the keyboard. Examples are: (A (! (1 (.
A jump is represented by )kn where n is a symbol which matches a label, and k is a condition code indicating what condition involving x or x and y must be true for the jump to occur. Valid condition codes are as follows:
Character	Jump occurs if	Comments
U	Unconditional	U stands for Unconditional
Z	x == 0	Z stands for Zero
N	x != 0	N stands for Non-zero
E	x == y	E stands for Equal
X	x != y	X looks like notequal sign
L	x <= y	L stands for less-than-or-equal
G	x >= y	G stands for greater-than-or-equal
M	Unconditional	M is Monitor; return to M5 prompt

EXAMPLES of valid jump symbols are: )UA )NI )X$ )G( (Z.
When a jump symbol is reached, the condition indicated by k is tested and if it is found to be true, a jump is made to the first occurrence of a label with the matching identifier symbol.
EXAMPLES
(i) 2000 (A “HELLO” £ )NA	Prints out “HELLO” 2000 times.
(ii) 0 (A =? “ “ & )NA	Prints out numbers from 0 to 65535 separated by spaces	(Thinks 65536=0).
(iii) (A )UA	Loops until reset is pressed.
(iv) 0=N (A N=? &=N , 5555 )GA	Prints out numbers from 0 to 5555..
WRITING PROGRAMS
M5 is a powerful language when all its features are properly understood, but it can be a little confusing for the beginner. There is fortunately an easy way of generating programs which can be used until familiarity with M5 is achieved. The method is to write the program in a more standard language and then translate into M5. While this method does not exploit the valuable “current variable” feature of M5, it will yield workable programs which are easier to follow in many ways. The program can then be optimised when it has started to work.
EXAMPLE A Program to print a table of squares from 1 to 20
BASIC	M5
10 PRINT “TABLE OF SQUARES"	“TABLE OF SQUARES
20 N=0	“ 0=N
30 N=N+1	(B N,1+=N
40 PRINT N, N*N	N=? “ “ N,N*=? “
50 IF N<>20 GOTO 30	“ N,20)XB
60 END	)M
NOTE: Newlines in output must be included between quotes in M5 programs. The numbers in M5 are not spaced on output, hence the space in the line equivalent to line 40.
The M5 produced will be completely sound and will run at about the same speed as the tiny Basic program.
If the M5 is optimised, keeping N in ”x" as much as possible and using the free layout and the & operator, the speed will be considerably faster, perhaps 4-5 times faster than a fast tiny basic.
Optimised:	“TABLE OF SQUARES
“ 0=N (B N&=N=? “ “,*=? “
“N,20 )XB )M
THE EDITOR
Introduction
The M5 Editor is entered by typing E when in the command mode. The edit prompt of E: will appear when the editor is ready to accept input. The editor will show the point where the last instruction was executed when it is entered by positioning a cursor at this location. The cursor is a shaded in square which is denoted here by a (underline). The cursor indicates the current position of the character pointer, and the character pointed at by the cursor appears at the top right of the screen. All manipulation of text is done relative to this cursor because there are no line numbers in M5.
The character indicating end of file in M5 is a null character which appears as a box when it is pointed at. A hazard in the M5 interpreter is that the pointer can be moved into the actual M5 Interpreter. A Rule must therefore be: DO NOT use any Delete or insert commands unless you can see where the pointer is positioned.
Commands
To manipulate the text of a program, the user must be able to position the cursor in the required area and then operate on the text. Commands to move the pointer are as follows:
>	Move cursor forward one place[1].
[1] > is shift-N, < is shift-M on the NASCOM under NASBUG T2/T4.
<	Move cursor backward one place.
R	Rewind – i.e., move cursor to the start of the file.
N	Move the cursor to the start of the next line (stop at end of prog.)
These commands may be repeated and if followed by a newline, will result in a printout of the text with the cursor in its new position.
EXAMPLE: You have typed in a program as follows:
(A "HELLO THERE " N=? " IS N
WHAT ZUMBER DO YOU WANT”... etc
And you want to move the cursor to the spelling error. Use: RN>>>>> i.e. move to start, move down a line, move in 5 characters. Using a space instead of a newline will not print out the text but will carry out the actions and return the edit prompt.
Once we have moved the prompt to where we want to make adjustments, we have commands to delete and insert characters:
D	Remove (delete) the character pointed at by the cursor. The cursor now points to the	next character along.
Innnn;	Insert the string nnnn before the character pointer. The terminator is a ; and the cursor	points to same character.
EXAMPLE: Edit ABCDERTYIJKLMNOP to replace RTY by FGH
ABCDERTYIJKLMNOP
E:R>>>>>	Move pointer to start then right 5 (to R)
ABCDE_TYIJKLMNOP	Character R appears at top R.H. side of screen.
E:D	Delete current character.
ABCDE_YIJKLMNOP	T appears at top right.
E:DD	Delete two more.
ABCDE_JKLMNOP	I appears at top right.
E:IFGH;	Insert correct characters.
ABCDEFGH_JKLMNOP	String now correct; I is still current character.
When editing is complete, the command W is used to return to command mode.
ERROR MESSAGES
When a large program is written concisely in M5, errors may be difficult to detect so good error diagnostics at runtime were included.
If a syntax error occurs, one of the following messages will appear:
SYM ERR x	The symbol x is not allowed in M5 (except in a string).
ID ERR x	The symbol x is not a valid identifier, and an attempt was made to	copy a value into it. (e.g. =x occurred.)
JID ERR x	The label x was not found when a jump occurred to it.
JC ERR x	The symbol x occurred in a jump condition position and is not a	valid code (one of U Z N E X L G M).
ERR x	The symbol x caused an error to occur. (Not one of above.)
In addition to giving the error type, the editing cursor is set up to point at the faulty symbol, so when the editor is entered from the monitor to correct the error, the cursor is in the correct position for amendments.
(N.B. in M6. JID errors are detected before the program starts to execute.)
SAMPLE PROGRAMS IN M5
Number summing program	(A”INPUT A NUMBER”?” THANKS
 NOW INPUT 2 MORE NUMBERS”?,”AND”?”GOOD!
 THEIR SUM IS”++=? “
 “)NA “THEIR SUM WAS ZERO – TYPE 0 FOR MORE FUN OR
 1 to END “?)ZA “GOODBYE!”)M

Factorial of a number	1=N ? )ZB (A =M , N* =N M£ )NA (B N=?

M5 24 hour clock:	)US (D N£=N )ND
(N.b. remove all spaces	H=?” HRS “M=?” MINS “S=?” SECS
for good timekeeping)	“ L=N S&=S , T )XD
 0=S M&=M , T )XD
 0=M H&=H , 24 )XD
 0=H )UD
(Start put at end)	(S 1750=L 60=T
“SET HRS”?=H”SET MINS”?=M”SECS”?=S”
“ )UD

Note that the main timing loop is at the beginning for higher speed. 1750 is the timekeeping constant, make smaller to speed up clock.

Square root of a number: 256=M ?=N (1 n,m/ , M )LS +,2/=M )U1
(S “ “M=?” “

Method used is very fast but a little hard to follow.

Prime numbers:	1=T
(N T&&=T
  1=G
(A G&&=G
  T,G/,G )GP
  @ )NA )UN
(P T=? “
  “ )UN

This can be compacted to only one line of course, (a bit baffling though ):

1=T (NT&&=T1=G(AG&&=GT,G/,G)GP@)NA)UN(PT=?“ “)UN
Hexadecimal object code listing 23 MAR 79 14.14

Addr Bytes Bytes
0C50 D6 3F CD 01 0E 5E 23 56 18 3B E1 ED 52 EB 18 35
0C60 C3 3E 0E EF 3F 00 21 00 00 CD 25 0E CD 14 0E 38
0C70 F8 EB 18 21 62 6B FD 21 0A 0E AF FD 46 01 FD 4E
0C80 00 ED 42 38 03 3C 18 F9 09 C6 30 CD 3B 01 FD 23
0C90 FD 23 0D 20 E5 DD 23 DD 7E 00 FE 20 28 F7 FE 1F
0CA0 28 F3 FE 3F 28 BD 30 A8 FE 2C 28 30 FE 3D 28 33
0CB0 FE 29 CA 74 0D FE 23 28 46 FE 26 28 3F FE 2B 28
0CC0 36 FE 2D 28 95 FE 2A 28 39 FE 2F 28 56 FE 28 28
0CD0 0E FE 22 28 6C B7 CA 3E 0E C3 54 0D D5 18 B6 DD
0CE0 23 18 B2 DD 23 DD 7E 00 D6 3F 28 88 DA C7 0D CD
0CF0 01 0E 73 23 72 18 9E E1 19 EB 18 99 13 18 96 1B
0D00 18 93 C1 3E 10 21 00 00 CB 7A 28 04 09 30 01 13
0D10 3D 28 09 EB 29 EB 29 30 EF 13 18 EC EB 22 C0 0B
0D20 C3 95 0C 42 4B 21 00 00 D1 3E 10 29 EB 29 EB 30
0D30 02 23 B7 ED 42 13 F2 3C 0D 09 CB 83 3D 20 EC 18
0D40 DC DD 23 DD 7E 00 FE 22 CA 95 0C B7 CA 3E 0E CD
0D50 3B 01 18 ED D6 30 FE 0A 30 13 21 00 00 DD 7E 00
0D60 DD 23 CD 14 0E 38 F6 EB DD 2B C3 97 0C EF 53 59
0D70 4D 00 18 57 DD 7E 01 FE 4E 28 31 FE 55 28 5B FE
0D80 5A 28 23 08 E1 E5 B7 ED 52 08 FE 45 28 24 FE 58
0D90 28 23 FE 4C 28 22 FE 47 28 23 FE 4D CA 3E 0E EF
0DA0 4A 00 DD 23 18 25 7A B3 28 30 18 14 7A B3 20 2A
0DB0 18 0E 08 18 F3 08 18 F6 08 30 1F 1B 03 08 38 1A
0DC0 DD 23 DD 23 C3 95 0C EF 49 44 00 EF 20 45 52 52
0DD0 20 00 DD 7E 00 CD 3B 01 18 64 DD 4E 02 31 FA 0F
0DE0 21 FE 0E 06 28 7E 23 B8 28 0D B7 C2 E5 0D DD 23
0DF0 DD 23 EF 4A 00 18 D0 7E B9 20 EA E5 DD E1 C3 95
0E00 0C 07 4F 06 00 21 BE 0B 09 C9 10 27 E8 03 64 00
0E10 0A 00 01 00 D6 30 FE 0A D0 29 54 5D 29 29 19 5F
0E20 16 00 19 37 C9 CD 3E 00 C3 3B 01 EF 1F 00 21 FD
0E30 0E 23 7E B7 C8 CD 3B 01 18 F7 AF 77 23 77 EF 1F
0E40 4D 35 3A 00 CD 25 0E FE 4C CC 2B 0E FE 49 CA D3
0E50 0E FE 52 20 09 EF 1F 00 DD 21 FD 0E 18 A0 FE 45
0E60 20 DC DD E5 E1 4E 36 7F E5 79 32 F6 0B CD 2B 0E
0E70 E1 71 EF 1F 45 3A 00 CD 25 0E FE 44 28 3A FE 1F
0E80 28 E3 FE 3E 20 01 23 FE 3C 20 01 2B FE 52 28 22
0E90 FE 4E 28 34 FE 57 28 A6 FE 49 20 DB CD 25 0E FE
0EA0 3B 28 D4 E5 4E 77 23 79 B7 20 F9 77 23 77 E1 23
0EB0 18 EA 21 FF 0E 2B 18 BF E5 DD E1 DD 7E 01 DD 77
0EC0 00 B7 28 B3 DD 23 18 F3 7E B7 28 AB 23 FE 1F 20
0ED0 F7 18 A4 EF 6E 70 75 74 1F 00 21 FD 0E 23 CD 25
0EE0 0E FE 3B CA 3A 0E 77 FE 1D 20 F2 2B 18 F0 D4

       Execute from 0C60. Program starts at 0EFF.